## Slide 1
A “new” VCA idea
make cleaner endmembers by averaging lots of matching pixels
CURRENTLY: trying to isolate the background
Brillouin spectroscopy data analysis
Notes: [Sources]
- User-provided project description and methodology (September 2026).

## Slide 2
The normal VCA endmember can just be one noisy pixel
2
one selected pixel
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
single pixel spectrum | 8 | 14 | 11 | 22 | 18 | 34 | 24 | 29 | 20 | 15
Problem: exposure time drives noise, so one pixel is a pretty bad definition of “pure”.
Notes: [Sources]
- User-provided project description and methodology (September 2026).

## Slide 3
Instead: find 3 “pure” spectra using groups of matching pixels
3
1
BACKGROUND
working now
2
CYTOPLASM (?)
later
3
NUCLEUS (?)
later
many similar pixels → add spectra together → less noise
Notes: [Sources]
- User-provided project description and methodology (September 2026).

## Slide 4
Step 1: define “probably background” from BFS values
4
background / medium
cell
Otsu line
take values BELOW this
1. sub-Otsu
rough background sample
↓
2. median
typical background BFS
↓
3. MAD × 1.4826
background noise width
↓
4. median + k·MAD
final cutoff (k = 2)
qualifies = inside the normal wobble of real background
Notes: [Sources]
- User-provided project description and methodology (September 2026).
- Histogram is a schematic visual, not measured project data.

## Slide 5
All qualifying background pixels become ONE endmember
5
bg 1
bg 2
bg 3
bg 4
bg 5
bg 6
bg 7
bg 8
SUM
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
summed background | 5 | 7 | 12 | 24 | 34 | 25 | 13 | 8 | 5
“pure” background endmember
same background chemistry, effectively more exposure time
Notes: [Sources]
- User-provided project description and methodology (September 2026).
- Spectrum is schematic, not measured project data.

## Slide 6
Quick test: does the constructed background behave better?
6
A
3 random dataset endmembers
INSERT RESULT IMAGE
(random + random + random)
B
2 random + constructed background
INSERT RESULT IMAGE
(random + random + summed BG)
Observed: the constructed endmember has much higher average potency in background pixels.
Notes: [Sources]
- User-provided project description and methodology (September 2026).

## Slide 7
So far: background looks like a real, reusable component
7
✓
background selected by a robust BFS cutoff
✓
many background spectra combined to reduce noise
✓
higher background potency than random-only VCA test
still exploratory / not finished
Notes: [Sources]
- User-provided project description and methodology (September 2026).

## Slide 8
Next: subtract the background spectrum
8
measured pixel spectrum
−
background endmember
=
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
measured | 8 | 13 | 24 | 42 | 35 | 28 | 21 | 10
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
background | 5 | 9 | 18 | 30 | 25 | 16 | 11 | 6
CELL-ONLY
SPECTRUM
(?)
Goal: remove the medium/background contribution before finding the other two endmembers.
Notes: [Sources]
- User-provided project description and methodology (September 2026).
- Spectra are schematic, not measured project data.

## Slide 9
Then isolate nucleus + cytoplasm, and rebuild the whole cell
9
BACKGROUND
spectrum
+
CYTOPLASM
spectrum
+
NUCLEUS
spectrum
entire cell = sum of 3 spectra
unfinished questions: separation rule? validation? potency stability across scans?
Notes: [Sources]
- User-provided project description and methodology (September 2026).